## Slide 1: Decarbonizing Steel Overview
Mimi Khawsam-ang, Max de Boer, Grace Frascati & Gernot Wagner
13 March 2024

## Slide 2: Steel sector overview: The problem

## Slide 3: Key messages Steel sector overview
The global steel sector is responsible for approximately 10% of global CO2e emissions
  Global steel emissions have more than doubled since 2000 (from 1.2 gigatonnes in 2000 to 2.5 gigatonnes in 2021). However, emissions have started to decouple from production levels since 2016
  Without intervention, emissions are expected to continue growing due to rising demand from emerging economies. Reaching net zero by 2050 would require a 25% emission reduction by 2030
Steel is currently produced through three main production routes, all of which emit CO2:
  Blast furnace-basic oxygen furnace (BF-BOF): 72% of global steel production. It uses coke and limestone to produce pure iron from iron ore in a blast furnace, which is then turned into steel in an oxygen furnace
  Scrap electric arc furnace (scrap EAF): 21% of global steel production. Scrap metal is melted in an EAF using electrical energy
  Natural gas-based direct reduced iron-electric arc furnace (NG DRI-EAF): 7% of global steel production. Iron ore is turned into iron using natural gas, which is then melted in an EAF to produce steel
On average, BF-BOF is the cheapest production method ($390 per tonne vs. $415 for scrap EAF and $455 for NG DRI-EAF). However, regional variations in costs (such as for raw material and fuel) make all three methods competitive
Because steel is a 100% recyclable material, increased use of scrap metal can help decarbonize the steel sector
Downstream activities after crude steelmaking (e.g., refining, casting, rolling) represent less than 20% of the total steel production emissions
Credit: Mimi Khawsam-ang, Max de Boer, Grace Frascati, and Gernot Wagner (22 February 2024); share/adapt with attribution. Contact: gwagner@columbia.edu

## Slide 4: Steel sector scope 1 and 2 emissions are ~10% of global emissions
40%
20%
80%
0%
100%
60%
Agricultural fuel combustion 4%
Crops
28%
Oil 4%
Land use, land-use change, and
forestry 14%
CO2e emissions in 2021: 50.1 billion tonnes
Livestock
33%
Natural gas
22%
Waste
21%
Agriculture, land use, and waste
Power and heat
Aviation 9%
Cement
17%
Marine 11%
Coal
74%
Other 2%
Chemicals
13%
Rail 1%
Industry
Road
77%
Transport
Oil and gas
20%
Commercial
combustion
21%
Commercial combustion 7%
HFCs from
refrigeration
and A/C
25%
Refining 4%
Residential
combustion
54%
Buildings
29%
29%
20%
15%
7%
Iron and steel
16%
Remaining industries
19%
Non-ferrous metals 2%
Non-metallic minerals 2%
Iron and steel
17%
Scope 1
Scope 2
Sources: Scope 1 emissions from Rhodium Group ClimateDeck (September 2023); Scope 2 iron and steel estimate from IEA (2023). Credit: Mimi Khawsam-ang, Max de Boer, Grace Frascati, and Gernot Wagner (22 February 2024); share/adapt with attribution. Contact: gwagner@columbia.edu

## Slide 5: Global steel emissions have more than doubled since 2000, with emission growth decoupled from production growth after 2016
Chart: 
 | 1.2377 | 1.2212 | 1.2401 | 1.305 | 1.3847 | 1.4997 | 1.5971 | 1.7643 | 1.7947 | 1.8037 | 2.0083 | 2.1675 | 2.1998 | 2.2949 | 2.3854 | 2.3237 | 2.2607 | 2.2838 | 2.4105 | 2.4624 | 2.3883 | 2.5173
 | 850 | 852 | 905 | 971 | 1063 | 1148 | 1250 | 1350 | 1345 | 1241 | 1435 | 1540 | 1563 | 1653 | 1675 | 1624 | 1633 | 1737 | 1828 | 1877 | 1882 | 1962
1
2
3
4
0
0
500
1,000
1,500
2,000
Global steel production (in million tonnes)
’00
‘01
’02
‘03
‘04
Global CO2e emissions from iron and steel production (in gigatonnes)
‘06
’07
‘08
‘09
‘10
‘11
‘12
‘13
‘14
‘15
‘16
‘17
‘18
‘19
‘20
‘21
‘05
Steel production
Iron and steel production emissions
Global CO2e emissions decoupled from steel production post-2016
Note: The majority of the world’s iron is used to make steel. Sources: Rhodium Group ClimateDeck (September 2023); World Steel Association; McKinsey, Decarbonization Challenge for Steel; IEA, CO2 Emissions in 2022, Reuters, China 2021 Crude Steel Output. Credit: Mimi Khawsam-ang, Max de Boer, Grace Frascati, and Gernot Wagner (22 February 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Observations
In recent years, the steel industry has made efforts to reduce its carbon footprint with more energy-efficient processes and technologies
  Though not enough by itself, recycling rates have improved (sitting around 80%-90% globally)
  Better manufacturing yields have made supply chains more efficient
  Enhanced control processes and predictive maintenance strategies have led improvements in operational efficiency
China, the largest steel producer in the world, saw a 3% decline in steel output in 2021 and a similar decline in the years since

## Slide 6: Crude steel is now produced through three main methods that all emit CO2:
Blast furnace-basic oxygen furnace (BF-BOF), which alone produces ~80% of iron & steel CO2
Scrap electric arc furnace (EAF), limited to recycled scrap
Natural gas-based direct reduced iron-electric arc furnace (NG DRI-EAF) most expensive, least used
1
2
3

## Slide 7: Of three main steelmaking methods, blast furnace-basic oxygen furnace (BF-BOF) is the cheapest, most popular, and most polluting
Sources: World Steel Association; IEEFA (2022); IEA, Iron and Steel Technology Roadmap (2020); Steel Technology, Basic Oxygen Furnace Steelmaking; Recycling Today, Growth of EAF Steelmaking; Wildsight, Do We Really Need Coal to Make Steel. Credit: Mimi Khawsam-ang, Max de Boer, Grace Frascati, and Gernot Wagner (22 February 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
BF-BOF ~73% of global steel production and ~80% of iron and steel CO2 emissions
Iron ore
Iron
Steel
2.33 tonnes of CO2 per tonne of steel
FeO2 + coal = Fe + CO2
1
Observations
BF-BOF: Iron ore, coke, and limestone produce iron in a blast furnace, which is turned into steel in an oxygen furnace

## Slide 8: Of the three main steelmaking methods, scrap electric arc furnace (EAF) is the cleanest, though limited by the scarcity of scrap material
More than 80% of steel recycled; scrap EAF accounts for ~22% of global steel production
Iron ore
Iron
Steel
Sources: World Steel Association; IEEFA (2022); IEA, Iron and Steel Technology Roadmap (2020); Steel Technology, Basic Oxygen Furnace Steelmaking; Recycling Today, Growth of EAF Steelmaking; Wildsight, Do We Really Need Coal to Make Steel. Credit: Mimi Khawsam-ang, Max de Boer, Grace Frascati, and Gernot Wagner (22 February 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Produces 0.66 tonnes of CO2 per tonne of crude steel, 72% less than BF-BOF
Takes collected scrap steel as input into an EAF
2
Observations
BF-BOF: Iron ore, coke, and limestone produce iron in a blast furnace, which is turned into steel in an oxygen furnace
Scrap EAF: Scrap metal is melted in an EAF using electrical energy

## Slide 9: Of the three main steelmaking methods, natural gas-based direct reduced iron-electric arc furnace (NG DRI-EAF) is the most expensive and least used
Iron ore
Iron
Steel
BF-BOF ~73% of global steel production and 80% of iron and steel CO2 emissions
Sources: World Steel Association; IEEFA (2022); IEA, Iron and Steel Technology Roadmap (2020); Steel Technology, Basic Oxygen Furnace Steelmaking; Recycling Today, Growth of EAF Steelmaking; Wildsight, Do We Really Need Coal to Make Steel. Credit: Mimi Khawsam-ang, Max de Boer, Grace Frascati, and Gernot Wagner (22 February 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Produces 1.39 tonnes of CO2 per tonne of crude steel, 40% less than BF-BOF
Uses natural gas, a cleaner reduction agent than coal
3
Observations
BF-BOF: Iron ore, coke, and limestone produce iron in a blast furnace, which is turned into steel in an oxygen furnace
Scrap EAF: Scrap metal is melted in an EAF using electrical energy
NG DRI-EAF: Iron ore turns into iron using natural gas, which is then melted in an EAF to produce steel

## Slide 10: At present, crude steel is produced through three main methods that all emit CO2: BF-BOF, scrap EAF, and NG DRI-EAF
Sources: World Steel Association; IEEFA (2022); IEA, Iron and Steel Technology Roadmap (2020); Steel Technology, Basic Oxygen Furnace Steelmaking; Recycling Today, Growth of EAF Steelmaking; Wildsight, Do We Really Need Coal to Make Steel. Credit: Mimi Khawsam-ang, Max de Boer, Grace Frascati, and Gernot Wagner (22 February 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
 | Blast Furnace-Basic Oxygen Furnace (BF-BOF) | Scrap Electric Arc Furnace (Scrap EAF) | Natural Gas-Based Direct Reduced Iron – Electric Arc Furnace (NG DRI-EAF)
Description | Iron ore, coke, and limestone produce pure iron in a blast furnace, which is turned into steel in an oxygen furnace | Scrap metal is melted in an EAF using electrical energy | Iron ore is turned into iron using natural gas, which is then melted in an EAF to produce steel
Main inputs | Iron ore, cooking coal | Scrap steel, electricity | Iron ore, natural gas
% of global steel production | 72% | 21% | 7%
CO2 per tonne of crude steel | 2.3 tonnes | 0.7 tonnes | 1.4 tonnes
Energy intensity per ton of crude steel | ~24 GJ | ~10 GJ | ~22 GJ
Average cost per tonne of crude steel | ~$390 | ~$415 | ~$455
Chart: 
 | 5 | 95
Chart: 
 | 22 | 78
Chart: 
 | 73 | 27
3
2
1

## Slide 11: Steel Decarbonization Technologies

## Slide 12: Key messages Steel decarbonization technologies
Credit: Mimi Khawsam-ang, Max de Boer, Grace Frascati, and Gernot Wagner (22 February 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Several emerging deep decarbonization steelmaking technologies now exist:
  Green hydrogen DRI-EAF: hydrogen produced using zero-carbon electricity is used as iron ore reductant instead of natural gas. Second step still uses an Electric Arc Furnace (EAF)
  Iron ore electrolysis: use of electricity to split pure iron from iron ore. Two technologies:
    Molten Oxide Electrolysis (MOE): a high current is run through a mixture of iron ore and a liquid electrolyte. The current causes the iron ore to split into oxygen and molten iron
    Electrowinning-EAF (EF-EAF): iron from iron ore is dissolved in an acid, which leaves behind impurities. The iron-rich solution is electrocuted to form pure solid iron, which is melted in an EAF
  Carbon Capture, Utilization and Storage (CCUS): BF-BOF and DRI-EAF can be retrofitted with point capture equipment. Captured carbon is then used or stored
These technologies produce steel with over 90% less CO2 emissions compared to conventional processes. However, green hydrogen DRI-EAF and CCUS BF-BOF / DRI-EAF come at a green price premium. CCUS is also less viable for BF route given difficulty to capture all carbon that’s released. Electrolysis may be cheaper than conventional processes, but has not been tested at scale yet
There are also some emerging transitional steelmaking technologies with lower decarbonization potential:
  Modifications to existing BF-BOF and DRI-EAF: using biomass as input, switching to zero-carbon electricity, partial green hydrogen injections
  Different production process: Smelting Reduction-BOF (SM-BOF)
Decarbonization potential of transitional technologies ranges between 10-50%, while they still come with a considerable green premium

## Slide 13: Most steel production uses BF-BOF, scrap EAF, and NG DRI-EAF, with Green H2 DRI-EAF, iron ore electrolysis, and CCUS technologies emerging
Iron ore
Iron
Steel
BF-BOF: Iron ore, coke, and limestone produce iron in a blast furnace, which is turned into steel in an oxygen furnace
Scrap EAF: Scrap metal is melted in an electric arc furnace using electrical energy
NG DRI-EAF: Iron ore turns into iron using natural gas, which is then melted in an EAF to produce steel
Green H2 DRI-EAF: Green hydrogen replaces natural gas as an iron ore reductant; water instead of CO2 is generated as a byproduct
Iron ore electrolysis: Molten oxide electrolysis runs a current through iron ore and liquid electrolyte to split ore into pure molten iron; electrowinning-EAF dissolves iron from iron ore in acid, then electrifies it from solid iron
Carbon capture, utilization, and storage (CCUS): Equipment is added to existing steel-producing infrastructure to capture emitted CO2, which is then sequestered or reused
See glossary. Sources: World Steel Association; IEEFA (2022); IEA, Iron and Steel Technology Roadmap (2020); Steel Technology, Basic Oxygen Furnace Steelmaking; Recycling Today, Growth of EAF Steelmaking; Wildsight, Do We Really Need Coal to Make Steel. Credit: Mimi Khawsam-ang, Max de Boer, Grace Frascati, and Gernot Wagner (22 February 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
2
1
3

## Slide 14: Green H2 DRI-EAF is an emerging technology using green hydrogen instead of natural gas as an iron ore reductant with standard electric arc furnaces
Green H2 direct reduced iron-EAF has an average cited decarbonization potential of ~90%
Iron ore
Iron
Steel
Sources: World Steel Association; IEEFA (2022); IEA, Iron and Steel Technology Roadmap (2020); Steel Technology, Basic Oxygen Furnace Steelmaking; Recycling Today, Growth of EAF Steelmaking; Wildsight, Do We Really Need Coal to Make Steel. Credit: Mimi Khawsam-ang, Max de Boer, Grace Frascati, and Gernot Wagner (22 February 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Renewable electricity is used throughout the production process, including the creation of green hydrogen
Comes at a green price premium
1
Observations
BF-BOF: Iron ore, coke, and limestone produce iron in a blast furnace, which is turned into steel in an oxygen furnace
Scrap EAF: Scrap metal is melted in an EAF using electrical energy
NG DRI-EAF: Iron ore turns into iron using natural gas, which is then melted in an EAF to produce steel
Green H2 DRI-EAF: Green hydrogen replaces natural gas as an iron ore reductant; byproduct is water vs. CO2

## Slide 15: Iron ore electrolysis is an emerging technology that uses an electric current to drive a chemical reaction, producing molten iron or pure solid iron
Iron ore electrolysis has an average cited decarbonization potential of ~97%
Iron ore
Iron
Steel
Sources: World Steel Association; IEEFA (2022); IEA, Iron and Steel Technology Roadmap (2020); Steel Technology, Basic Oxygen Furnace Steelmaking; Recycling Today, Growth of EAF Steelmaking; Wildsight, Do We Really Need Coal to Make Steel. Credit: Mimi Khawsam-ang, Max de Boer, Grace Frascati, and Gernot Wagner (13 March 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Iron is now akin to solid-state battery, allowing for a reversed process that produces electricity
Electrowinning-EAF dissolves iron from iron ore in acid, then electrifies it to form pure solid iron; molten oxide electrolysis runs a current through iron ore and liquid electrolyte to split ore into pure molten iron
May be cheaper than conventional processes but has not yet been proven at scale
2
Observations
BF-BOF: Iron ore, coke, and limestone produce iron in a blast furnace, which is turned into steel in an oxygen furnace
Scrap EAF: Scrap metal is melted in an electric arc furnace (EAF) using electrical energy
NG DRI-EAF: Iron ore turns into iron using natural gas, which is then melted in an EAF to produce steel
Green H2 DRI-EAF: Green hydrogen replaces natural gas as an iron ore reductant; byproduct is water vs. CO2
Iron ore electrolysis: Molten oxide electrolysis runs a current through iron ore and liquid electrolyte to split ore into pure molten iron; electrowinning-EAF dissolves iron from iron ore in acid, then electrifies it to form solid iron

## Slide 16: Carbon capture, utilization, and storage (CCUS) is an emerging technology that reduces steel’s carbon footprint by capturing released CO2
Iron ore
Iron
Steel
Despite a cited ~90% decarbonization potential, CCUS technology is largely unproven
Sources: World Steel Association; IEEFA (2022); IEA, Iron and Steel Technology Roadmap (2020); Steel Technology, Basic Oxygen Furnace Steelmaking; Recycling Today, Growth of EAF Steelmaking; Wildsight, Do We Really Need Coal to Make Steel. Credit: Mimi Khawsam-ang, Max de Boer, Grace Frascati, and Gernot Wagner (22 February 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Less viable for the blast furnace route given difficulty of capturing all carbon released
Capture rates range from 50%-90%, and viability is debated due to the lack of a single capture point
3
Observations
BF-BOF: Iron ore, coke, and limestone produce iron in a blast furnace, which is turned into steel in an oxygen furnace
Scrap EAF: Scrap metal is melted in an electric arc furnace using electrical energy
NG DRI-EAF: Iron ore turns into iron using natural gas, which is then melted in an EAF to produce steel
Green H2 DRI-EAF: Green hydrogen replaces natural gas as an iron ore reductant; byproduct is water vs. CO2
Iron ore electrolysis: Molten oxide electrolysis runs a current through iron ore and liquid electrolytes to split ore into pure molten iron; electrowinning-EAF dissolves iron from iron ore in acid, then electrifies it to form solid iron
CCUS: Equipment is added to existing steel-producing infrastructure to capture emitted CO2, to then sequester or reuse

## Slide 17: Green H2, electrolysis, and CCUS could reduce steelmaking CO2 emissions by over 85% if implemented at scale
 | 100% Green Hydrogen (H2) DRI-EAF | Iron Ore Electrolysis | Carbon Capture, Utilization, and Storage (CCUS)
Description | Green hydrogen replaces natural gas as an iron ore reductant in DRI shaft; the rest of the process remains the same Generates water as a byproduct instead of CO2 | Two different processes are possible: Molten oxide electrolysis: High current runs through mixture of iron ore and liquid electrolyte to split ore into pure molten iron Electrowinning-EAF: Iron from iron ore is dissolved in acid. Iron-rich solution is then electrified to form pure solid iron | CCUS equipment can be added to existing steel-producing infrastructure to capture emitted CO2 Captured CO2 is then sequestered underground or reused
Real-time sector initiatives | HYBRIT 100% fossil fuel-free DRI-EAF production with green H2 used for DRI | Electra Electrowinning to produce high-purity iron plates ready for EAF input (no DRI or MOE step) | ArcelorMittal Carbalyst® captures carbon from a blast furnace and reuses it as bio-ethanol. However, technology not proven at scale
Applicability to conventional routes | Applicable to existing DRI-EAF route, with minor retrofitting | Full overhaul of BF-BOF equipment required; replacement of DRI shaft in DRI-EAF | Retrofitting of capture technology is possible on conventional BF-BOF and DRI-EAF
Decarbonization potential (vs. BF-BOF) | ~90% | ~97% | ~90%
Estimated production cost (excl. CapEx) | <$800 per tonne of steel | ~$215 per tonne of iron + cost of ‘stranded’ iron ore | ~$380 – 400 per tonne
3
2
1
Sources: Columbia Center on Global Energy Policy (2021); IEA, Iron and Steel Technology Roadmap (2020); McKinsey (2020); Mining Technology (2023); Tata Steel; Primetals Technologies;
Edie, ArcelorMittal accused of net-zero greenwashing (2023). Credit: Mimi Khawsam-ang, Max de Boer, Grace Frascati, and Gernot Wagner (13 March 2024); share/adapt with attribution.
Contact: gwagner@columbia.edu
Hypothetical best-case scenario

## Slide 18: Green H2, electrolysis, and CCUS could reduce steelmaking CO2 emissions by over 85% if implemented at scale
Sources: Columbia Center on Global Energy Policy (2021); American Institute of Chemical Engineers (2023); Electra; Boston Metal; Midrex (2021); International Journal of Greenhouse Gas Control Volume 61 (2017); Mission Possible Partnership Net Zero Steel Sector Transition Strategy (2021). Credit: Mimi Khawsam-ang, Max de Boer, Grace Frascati, and Gernot Wagner (22 February 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Chart: 
 | 89.84 | 97 | 90
 | 85 | 95.57 | 90
0
20
40
60
80
100
Crude steelmaking CO2 emissions reduction potential of deep decarbonization technologies relative to conventional BF-BOF and NG DRI-EAF routes (in %)
Green H2 DRI-EAF
(Zero-carbon elec.)
Electrolysis
(Zero-carbon elec.)
CCUS Additions
97
96
CO2 Reduction Potential (vs. Conventional BF-BOF)
CO2 Reduction Potential (vs. Conventional NG DRI-EAF)
All discussed technologies have a CO2 reduction potential of >85%
  Hypothetical best-case scenario
Observations
A key enabler for green steel production is an abundance of green electricity, which is required for both powering electrolysis and the production of green hydrogen
  Assuming the current global electricity mix does not change, H2 DRI-EAF would have a decarbonization potential of only 60% instead of >85% when 100% green electricity is used
The 90% CO2 reduction for CCUS is a hypothetical best-case scenario, which at present has not been proven at scale

## Slide 19: Steel decarbonization technologies, however, often come with a green premium and require large amounts of green energy
Chart: 
 | 800 | 400 | 380 | 365 | 325 | 215
200
400
600
800
1,000
0
Green H2 DRI-EAF
Average steel production cost estimates per technology (excluding CapEx) at current price levels (USD per tonne)
CCUS (BF-BOF)
DRI-EAF
BF-BOF
Electrolysis
~380
~365
CCUS (DRI-EAF)
Note: Electrolysis costs are assumed to see a 15% reduction relative to BF-BOF. Carbon capture costs as $25/tonne-CO2 with a ~90% capture rate. Green H2 price at $6.40/kg. Sources: Columbia Center on Global Energy Policy (2021); Boston Metal; MIT (2018); Journal of Cleaner Production Volume 389 (2023); IEA, Is carbon capture too expensive? (2021); McKinsey (2020); Nature Energy (2022); IEA, Iron and Steel Technology Roadmap (2020). Credit: Mimi Khawsam-ang, Max de Boer, Grace Frascati, and Gernot Wagner (13 March 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Decarbonization technologies
Conventional technologies
Green technologies often come at a green premium
  Hypothetical best-case scenario
Observations
Green H2 DRI-EAF
Green H2 prices are expected to fall >50%, to $2.20-$2.90 per kg by 2030, making H2 DRI-EAF adoption much more attractive
Switching from BF-BOF to green H2 DRI-EAF is costly without government support. CapEx required for a new plant ranges from $1.1 billion to $1.7 billion and operating expenses are higher
Electrolysis/Electrowinning
Claimed cost savings compared to conventional steel production methods are still uncertain due to the nascency of technology
At present, there is not enough green electricity available on grids to support large-scale electrolysis-based steelmaking
CCUS
According to the IEA, CCUS retrofits are at present the most advanced and cost-effective low-carbon solutions for the steel industry
Adding CCUS technology to existing plants is expected to require only minor modifications

## Slide 20: Other transitional decarbonization technologies take less time and effort to implement but have lower decarbonization potential
 | MODIFICATIONS TO BF-BOF / DRI-EAF PROCESSES |  |  | NEW PRODUCTION PROCESS
 | Biomass as input | Switch to zero-carbon electricity | Partial green hydrogen injections | Smelting Reduction BOF (SR-BOF)
Process description | Biomass used as substitute for coal in BF-BOF Biosyngas used as substitute for natural gas in DRI shaft | Switch from fossil-fueled electricity to 100% green electricity >60% electricity generation is fossil fuel-based today | Injection of hydrogen (~5-10%) to reduce coal use in BF Injection of hydrogen (~30%) to reduce natural gas use in DRI shaft | Production process that eliminates need for coke making and iron ore sintering Emits less CO2 than regular BF-BOF
Decarbonization potential (vs. BF-BOF) | ~40% | ~5 – 40% | ~20% | ~20%
Estimated production costs / tonne (excl. CAPEX) | ~$455 – 700 | ~$345 – 435 | ~$375 – 495 | ~$310
Limits to decarbonization | Insufficient sustainable biomass is likely available to enable a global transition to this production method | Direct process emissions from BF-BOF and DRI-EAF are not addressed | There is a limit to how much H2 can be injected without replacing production equipment | Coal, a primary input, emits CO2, but smelting reduction-BOF provides a concentrated CO2 stream, ideal for capture
Source: IEA Iron and Steel Technology Roadmap (2020), World Steel Association (2021), Energy Institute Statistical Review of World Energy (2023), Columbia Center on Global Energy Policy (2021)
Journal of Cleaner Production Volume 393 (2023). Credit: Mimi Khawsam-ang, Max de Boer, Grace Frascati & Gernot Wagner (22 February 2024); share/adapt with attribution.
Contact: gwagner@columbia.edu

## Slide 21: Adoption trends & obstacles

## Slide 22: Key messages Steel’s future
Credit: Mimi Khawsam-ang, Max de Boer, Grace Frascati, and Gernot Wagner (22 February 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Reaching net zero by 2050 would require a ~25% emissions reduction by 2030
Policymakers can and should step in to assist with green technologies, such as H2 Green Steel’s and Electra’s new generation plants
The focus should be on creating low-cost, low-carbon electricity and on driving down capital costs for new technologies
Time is of the essence, as Asia’s large fleet of high-carbon legacy blast furnaces (~75% of global iron production) are due for costly relining in the next 10 years. This presents an opportunity to instead invest in newer, greener technologies
A production tax credit for low-emission iron would support electrolysis as well as green H2

## Slide 23: Appendix

## Slide 24: Glossary
BAU | Business as usual
BF-BOF | Blast Furnace-Basic Oxygen Furnace
CAPEX | Capital expenditure(s)
CCUS | Carbon capture, utilization & storage
CO | Carbon monoxide
CO2 | Carbon dioxide
CO2e | CO2 equivalent, using global warming potential as conversion factor
DAC | Direct Air Capture
DRI-EAF | Direct Reduced Iron-Electric Arc Furnace production process
EAF | Electric Arc Furnace
EBITDA | Earnings before interest, taxes, depreciation, and amortization
EW-EAF | Electrowinning-Electric Arc Furnace
Gt | Gigatonne, equal to 1 billion metric tonnes
H2 | Hydrogen
IEA | International Energy Agency
HRC | Hot Rolled Coil (type of finished steel product)
MPP | Mission Possible Partnership – industry decarbonization coalition
MOE | Molten oxide electrolysis
NG | Natural gas
NAFTA | North American Free-Trade Agreement
NG | Natural gas
NG DRI-EAF | DRI-EAF production process using natural gas
NZE | Net Zero Emissions
O2 | Oxygen
OECD | The Organization for Economic Cooperation and Development
OPEX | Operational expenditure(s)
SR-BOF | Smelting Reduction-Basic Oxygen Furnace
Tonne | Metric ton